## Slide 1: Centralized Temperature & Humidity Monitoring System for Server Racks
IoT with ESP32 Training
IoT with ESP32 Training|Rev01-JAN2021|Loc/Date
Rack 1
50 °C
60%
Rack 2
50 °C
60%
MODULE 2d
https://www.upsite.com/blog/sealing-rack-need/
Rack 3
54 °C
70%

## Slide 2
This tutorial will teach how to save data from ESP32s (or any ethernet microcontrollers) into MySQL.
Scenario:
You are required to monitor 2 server racks in a data center; i.e., Rack#1 & Rack#2 by using 2 ESP32s and 2 DHT11 sensors. Both readings need to be saved into a single table. The temperature & humidity of both rooms can be monitored thru webpage.
Project Overview
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
Rev01 JAN2021
ZXZXZ

## Slide 3
Hardware:
 1 x ESP-32 Wifi+Bluetooth 2-In-1 Development Board for Arduino (30 pin) + Cable.
 1 x Temperature & Humidity Sensor, DHT11.
 Jumpers (male to female).
 2 x Mini Breadboard.
Software:
 XAMPP ver 8.0.1(PHP 8.0.1) for Windows / OS X.
Components
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks

## Slide 4
Solution
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Step 1: Propose block diagram & flowcharts
A story board of the whole project which will give clear picture what you need to do.
 Step 2: Install Apache Web Server
i. Install XAMPP (once), start web server service
ii. Start XAMPP service
iii. Test XAMPP page & PHPMyAdmin page
 Step 3: Creating MySQL Database
i. Create database + test
ii. Create a PHP file for medium of transferring information from ESP32 to MySQL + Test
**Test with dummy data / manually inject data to database
 Step 4: Preparing PHP script to insert data to MySQL database
i. Configure *.php scripts.
ii. PHP script to display database.
iii. HTTP GET & HTTP POST.

## Slide 5
Solution
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Step 4: Preparing PHP script to insert data to MySQL database
i. Configure esp_to_dbase.php file.
ii. PHP script to display database.
 Step 2: Install XAMPP
i. Install XAMPP (once)
ii. Start XAMPP service
iii. Test XAMPP page & PHPMyAdmin page
 Step 3: Creating MySQL Database
i. Create database + test
iii. Create a PHP file for medium of transferring information from ESP32 to MySQL + Test
**Test with dummy data / manually inject data to database
 Step 3: x Temperature & Humidity Sensor, DHT11.
i. Construct circuit
ii.
 Step 4: Integrate Step 1 & Step 2
i. Construct circuit

## Slide 6
Project Block Diagram
Solution: Step 1
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
Router
XAMPP Server
DHT11
Sensor
ESP32
PROPOSED BLOCK DIAGRAM & FLOWCHART

## Slide 7
Flowchart
Solution: Step 1
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
Connect to WiFi
Start
Block Diagram
Microcontroller;
Input: Temperature, Humidity, RacklD
Initialize DHT11
End
T
T
F
F
Start
Install & execute XAMPP
T
F
Database: datacenters_ctivities
Table: room_dc230
Fields: id, timeIndateIn, rackID, temp, humid, status
Insert Data Manually
End
Success
F
Test .php by manually inject rackID, temp,humid & status into database
Success
Fail
PROPOSED BLOCK DIAGRAM & FLOWCHART

## Slide 8
Flowchart
Solution: Step 1
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
Connect to WiFi
Start
Save data in MySQL
Initialize DHT11
End
T
T
F
F
Start
Install & execute XAMPP
T
F
Database: datacenters_ctivities
Table: room_dc230
Fields: id, timeIndateIn, rackID, temp, humid, status
Insert Data Manually
End
Success
F
Test .php by manually inject rackID, temp,humid & status into database
Success
Fail
PROPOSED BLOCK DIAGRAM & FLOWCHART

## Slide 9
Solution: Step 2
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Download and install latest version of XAMPP from https://www.apachefriends.org/download.html
 This link shows full tutorial on installing XAMPP on windows https://blog.templatetoaster.com/install-xampp-on-windows/
 Once installed, launch XAMMP Control Panel (7.3.26)
For Windows (v7.3.26):
- to run, go to c://xampp/contol-control.exe  Start MySQL Database & Apache Web Service
- open your browser and type http://localhost/
Click START
SERVICE
STARTED
INSTALL, START & TEST XAMPP SERVICES

## Slide 10
Solution: Step 2
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
For OS X (v7.3.0):
- go to Applications>XAMPP>manager-osx  Start MySQL Database & Apache Web Service
- open your browser and type http://localhost/
Click START
SERVICE
STARTED
INSTALL, START & TEST XAMPP SERVICES

## Slide 11
Solution: Step 2
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 XAMPP landing page can be found at http://localhost/
Windows system
OS X system
INSTALL, START & TEST XAMPP SERVICES

## Slide 12
Solution: Step 2
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 To use MySQL database, point your browser to http://localhost/phpmyadmin
 You can also click phpMyAdmin link at XAMPP dashboard.
 PHPMyAdmin is a third party tool to manage data inside the database.
INSTALL, START & TEST XAMPP SERVICES

## Slide 13
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Set up database with the following properties:
Database Name: datacenter_activities
Table Name: room_dc230
Columns: 6
NAME | TYPE | LENGTH | ADDITIONAL SETTING
id | INT | 11 | Index: PRIMARY AI: YES
logDateTime | DATETIME | - | Default: CURRENT_TIMESTAMP
rackID | VARCHAR | 255 | -
tempValue | VARCHAR | 255 | -
humidValue | VARCHAR | 255 | -
rackStatus | VARCHAR | 255 | -
AI = Auto Increment
- = empty
#use appropriate name for variables (dbname, tablename…) that reflect with the task/activity
https://www.javatpoint.com/creating-mysql-database-with-xampp
CREATING MySQL DATABASE

## Slide 14
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Database Name: datacenter_activities
Existing databases
5
6
1
2
3
1
CREATING MySQL DATABASE

## Slide 15
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Table Name: room_ds230 Number of columns: 6
4
5
6
Just created
CREATING MySQL DATABASE

## Slide 16
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Table Name: room_ds230 Number of columns: 6
7
8
9
10
11
12
13
14
15
16
17
19
20
18
21
22
23
24
25
26
27
28
CREATING MySQL DATABASE

## Slide 17
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 What you should know on PHPMyAdmin panel (at least).
a
b
c
d
e
Browse  to view / edit / delete data stored in room_dc230, increment counter will proceed to next number.
Structure  to view / edit / delete / add table structure.
Insert  to manually insert data into room_dc230.
Empty  to empty room_dc230 database, any increment counter will start from 1.
Drop  will delete room_dc230 table.
b
CREATING MySQL DATABASE

## Slide 18
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Click Browse to view room_dc230 database. It is empty since no data in it.
a
a
b
c
An empty database
CREATING MySQL DATABASE

## Slide 19
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 In order to insert data manually into room_dc230, select Insert.
 For this time, leave ALL text box empty. Then click Go to save into room_dc230 database.
c
CREATING MySQL DATABASE

## Slide 20
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Observe the red arrow. What do you think?
 Click Browse link to view the input.
a
Blank data inserted into rackID, tempValue, humidValue & rackStatus
a
CREATING MySQL DATABASE

## Slide 21
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Congrats! You managed to add your first data into room_dc230 database.
 Click Edit link if you wish to edit the data.
 Delete will not reset the id into zero. Next data entered will get the following running number.
a
CREATING MySQL DATABASE

## Slide 22
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Go to Insert link and add the information as show by red arrow & press Go to save the data.
1
2
3
4
5
CREATING MySQL DATABASE

## Slide 23
Solution: Step 3
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Red arrow shows the new data that have been entered.
CREATING MySQL DATABASE

## Slide 24
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Two PHP files are needed; esptodb.php & webview.php.
ESP32 + DHT11
HTTP POST
http://localhost/a-my/esptodb.php
Database: datacenters_activities
Table: room_dc230
ESP32 + DHT11
Insert racks’ information into database table
...
**esptodb.php is the medium of ESP32 to save information from racks into database
** webview.php is to display datacenters activities on web page.
http://localhost/a-my/webview.php
Publish information upon web request
Send every xx seconds
Update every xx seconds
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 25
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 In order to publish any website either PHP or HTML, you need to save the files in a specific folder, named htdocs. It can be found in XAMPP folder.
 It is advised that each project has its own folder. This may avoid you to override files that carries same filename.
1
2
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 26
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Navigate to htdocs & create new folder named a-my.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 27
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Download “esptodb.php“ & “webview.php” from http://bit.ly/3p2pmNd.
 Extract & paste the files into a-my folder.
 ESP32 will use “esptodb.php“ as a medium to save information into MySQL while client will use “webview.php” to view the information thru web browsers.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 28
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Open up your web browser & type localhost/a-my/ in the address bar. You should get the similar output. If you failed to see this, go to your XAMPP C-Panel & check whether the server services has been deployed or not.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 29
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Click at the file one at a time. There are errors/warnings since the files were not properly configure.
 You need a text editor to edit both files & we are going to use Sublime Text as the editor for PHP scripts. You may download it the following link: https://www.sublimetext.com/3
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 30
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Open webview.php with sublimetext or any preferable text editor. The credentials are to establish connection to the database.
 By default, $servername is “localhost” & $username is “root”.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 31
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Before getting access to MySQL database, the client must establish a connection to the server as shown in Line#30. If any of the credentials incorrect, the client don’t have the permission to access the server. The script stops & will display error message at the browser. (MySQLi = MySQL improved)
 Line#36 indicates selection of 5 columns from room_dc230 table with descending order of id. The syntax is put into a variable called $sql.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 32
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 A mix of PHP and HTML syntax in creating table.
 Line#47 – Line#69 is hosting asking, fetch data from database & display them in table manner.
”query( )” is a function that fetch data that was assigned in $sql variable. The results were put into a variable called $results.
 each data from ”$results” will be split into an array form according to its respected field.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 33
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Script to display the information fetched from database in table form. Each row represent 1 set data / reading. New row carries another set of reading/data.
 The fetched data in $result are emptied, thus the variable carries no information.
 ”close( )” is a function that closes previously open database connection.
 End of HTML script.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 34
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Open esptodb.php with sublimetext or any preferable text editor. Fill up with your database credentials.
 If webview.php is meant for client to view the temperature & humidity of the racks, esptodb.php is a script for EPS32 saving the racks data into the database.
 $api_key_value is a kind of password to except information send from the ESP32. ESP32 must send same key & the information will only be entertained when the key is matched. Otherwise, the information will be rejected.
 Line#33 will empty the content of the handlers. The task of the handlers are to keep for information temporarily when received from the ESP32 thru HTTP POST or HTTP GET request.
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 35
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 There are 2 types of Hyper Text Transfer Protocol (HTTP) request methods: POST & GET.
 What is HTTP? HTTP works as request-response protocol between a client & a server.
 HTTP GET is used to request data from a specified resource. It is often used to get values form APIs.
  - eg., http://localhost/esptodb.php?key=“tPmAT5Ab3jF9&temp=10
  - Name = Key & value = tPmAT5Ab3jF9 + name = temp & value = 10 are send together in URL
  - With HTPP GET, data is visible to everyone
 HTTP POST is used to send information to a server to create/update a resource.
  - eg., publish sensor readings to a server
  - The data sent to the server with POST is stored in the request body of the HTTP request
  - String serverPath = serverName "?temperature=24.37"; // sample in sketch
  - With HTTP POST, data is not visible in the URL request. However, if it’s not encrypted, it’s still visible in the request body.
(With HTTP POST, data is not visible in the URL request. However, if it’s not encrypted, it’s still visible in the request body.)
https://randomnerdtutorials.com/esp8266-nodemcu-http-get-post-arduino/
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 36
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
http://localhost/a-my/esptodbase.php?api_key=tPmAT5Ab3j7F9&rID=v112&temp=22&humid=40&currentStat=NORMAL
a
a
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST

## Slide 37
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST
 It is now the time to test both PHP scripts. Make sure that the database credentials have set accordingly.
 No information print out since the database is still empty.

## Slide 38
Solution: Step 4
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
PHP SCRIPTS & HTDOCS & CODE EXPLAINATION & RUN TEST
 Open a browser, then copy & paste the following link & press enter.
http://localhost/a-my/esptodb.php?api_key=tPmAT5Ab3j7F9&rID=v112&temp=22&humid=40&currentStat=NORMAL
 Try this:
1- http://localhost/a-my/
2- http://localhost/a-my/esptodb.php?api_key=tpMAT5Ab3j7F9&rID=v111&temp=22.4&humid=40%&currentStat=“NORMAL”

## Slide 39
Solution: Step 5
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Open sketch-v_esp32-dht11-http-post.ino from http://bit.ly/3p2pmNd downloaded in Step 4. Do not upload the sketch since you need to make some changes.
 This will inform the compiler to compile the correct library no matter if what board you are currently uploading into. In this case, either ESP32 or NodeMCU & ESP8266.
ESP32 POST INFORMATION TO DBASE: SKETCH WALKTHROUGH

## Slide 40
Solution: Step 5
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 Set the followings to the WiFi network connection.
ESP32 POST INFORMATION TO DBASE: SKETCH WALKTHROUGH
 Change the “192.168.1.102” with your server’s IP address. How to find IP address of your system ?
 The file path “/a-my/esptodb.php” reflects the “drive/xampp/htdocs/” & set in STEP xx.
 Both ESP32 has the same API key with esptodb.php to avoid fake request. If not match, the information will not save into database. The API key is manually generated by the developer/user.
 Set the sensorID accordingly – e.g. rackID. This ID must be different from one another & must be documented, easier to detect & locate.

## Slide 41
Solution: Step 5
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
 The board will connect to the WiFi router. If any of the SSID or Password is incorrect, the board will not to join the network. Open Serial Monitor to view the process. IP address will be published if the board connected to the router.
ESP32 POST INFORMATION TO DBASE: SKETCH WALKTHROUGH
 Fail to connect to router.

## Slide 42
Solution: Step 5
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
ESP32 POST INFORMATION TO DBASE: SKETCH WALKTHROUGH
 Fail to connect to router.
#66: Test send data to esptodb.php (IP add at #29)
#81: Success to communicate with server
#85: Unable to communicate with server --> not in the same network
#96: Update every 30 seconds
#51
#50
#47
#67
#68
#86
#87
#82
#83

## Slide 43
Solution: Step 6
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
SCHEMATIC DIAGRAM
GND
Vin
Signal D4
 After success tested the skech, its time to combine the DHT part with ESP32.
 Before we go any further, construct the circuit as in the figure.
 Check a few times, the connections that have been made before plugging ESP32 to USB port. This might prevent short circuit to DHT11. Watch out on sensors’ pin. Same type, doesn’t mean same pin configurations.

## Slide 44
Solution: Step 7
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
THE WORKING SKETCH
 Open sketch-vii_esp32-dht11-http-post.ino from http://bit.ly/3p2pmNd downloaded in Step 4. Do not upload the sketch since you need to make some changes.

## Slide 45
Solution: Step 7
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
THE WORKING SKETCH

## Slide 46
Solution: Step 7
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
THE WORKING SKETCH

## Slide 47
Solution: Step 7
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
THE WORKING SKETCH

## Slide 48
Solution: Step 7
Rev01 JAN2021
2d. Centralized Temperature & Humidity Monitoring System for Server Racks
THE WORKING SKETCH

## Slide 49
QUESTIONS?
Questions?
2d. Monitoring Data Center Temperature & Humidity Level
Rev01 JAN2021

## Slide 50
EXERCISE
Modify this project by doing the followings:
Add LED statement in ESP32 sketch – if connected to WiFi, built in led (GPIO2) will switch on.
Write condition statements at PHP files:
  If temp > 30˚C status is ALERT
  If temp > 40˚C status is DANGER
  The status need to be saved in the database together with other information.
  HINT: you need to omit the status information from ESP32 skech.
2d. Monitoring Data Center Temperature & Humidity Level
Rev01 JAN2021